## Slide 1
The life history of a
double star telescope
Bob Argyle

## Slide 2: Brief resumé of talk
Double and binary stars
The maker: Thomas Cooke
The telescope
The first user: William Rutter Dawes
The telescope moves on: George Hunt, William Maw, W. J. Thorrowgood
Coming to Cambridge
The current observing programme
Results; measurement accuracy
Publication and current amateur journals

## Slide 3: Binary stars
Gravitationally connected
Multiple stars and hierarchies
Majority of nearby stars are in double or multiple
systems
Periods range from 5 minutes to millions of years
‘Visual’ binaries are usually separated by less
than 5 seconds of arc

## Slide 5: Optical pairs and binary stars
Optical pairs – a chance alignment
Examples delta Herculis

## Slide 6: Orbits of Sirius A and B

## Slide 7: Thomas Cooke 1807 - 1868
Set up business in York in 1837
Built a number of refractors up to 15-inch (and exceptionally 25-inch)
Also built turret clocks and a 3 wheeled steam driven car
Asked by Dawes to build an 8-inch in 1863
Delivered the OG personally in Oct 1864

## Slide 8: Thorrowgood telescope
Built York, England in 1864
Aperture: 8-inches (20-cm)
Focal length: 114 inches (2900-cm) = f/14
New objective fitted 1865
Weight-driven clock drive
Little used by Dawes before his death (1868)

## Slide 10: William Rutter Dawes (1799-1868)

## Slide 11: W. R. Dawes - 1
Trained as a physician at St Barts, London
Moved to Liverpool in 1826, met William Lassell and became interested in astronomy
Observer at George Bishop’s observatory (1839 – 1844)
Co-discovered the Crêpe Ring of Saturn (with Bond)
Received Gold Medal of RAS in 1855 for his work on
double stars

## Slide 13: Airy’s Gold Medal address 1855
``Distinguished as Mr Dawes has been by an extraordinary acuteness of vision, and by a habitual, and (as I may say) contemplative precision in the use of his instruments, his observations have commanded a degree of respect which has not often been obtained by the productions of larger instruments”

## Slide 14: W. R. Dawes - 2
Moved to Haddenham (Bucks) in 1857
Bought the telescope from Cooke in 1864
Rarely used it before his death
Derived the Dawes Limit (4”.56/d) which applied to equally bright double stars in a small refractor
Completed his catalogue of double star measures just before his death

## Slide 15: Derivation of the Dawes Limit QJRAS 1867

## Slide 16: Dawes limit

## Slide 17: Rayleigh limit

## Slide 18: Dawes limit (empirical)
Usually defined as 4”.56/d(in)
Diameter Resolution
(cm) (arc secs)
10 1.16
20 0.58
30 0.39
40 0.29
100 0.12

## Slide 19: Practical limits of resolution
Lewis found:
Equal bright pairs (5.7, 6.4) 4”.8/d
Equal faint pairs (8.5, 9.1) 8”.5/d
Unequal pairs (6.2, 9.5) 16”.5/d
Very unequal pairs (4.7, 10.4 36”.0/d
But Aitken found for
Equal bright pairs (6.9, 7.1) 4”.3/d
Equal faint pairs (8.8, 9.0) 6”.1/d

## Slide 20: Improvement in resolution
Separation Period
Almagest (140AD) 11 arc mins
First telescopic pair (1617) 15 arc secs 15000 years
Herschel (1800) 0.5 arc sec 50 years
Burnham and Aitken (1900) 0.1 arc sec 5 years
Michelson (1920’s) 0.05 arc sec 100 days
McAlister (speckle) 0.03 arc sec
Ground-based arrays
NPOI 0.004 arc sec 4 days
SUSI 0.00005 arc sec hours

## Slide 21: The telescope moves on
Dawes offered the telescope to Cambridge Observatory in 1867 for £580
J. C. Adams considered it the equal of Struve’s 9.3-inch at Dorpat
The University Regents decided not to proceed with the purchase
It was then sold to George Hunt who used it infrequently – on his death it passed to W H Maw

## Slide 22: George Hunt FRAS (1823 - 1896)
Family involved in ironworks and collieries
Bought the telescope in 1869 and erected it in Edgbaston, later moving to Dulwich
Wrote more than 20 papers on a range of topics
Between 1869 and 1894

## Slide 23: William Henry Maw (1838 - 1924)
Started work as draughtsman in railway office
Rose to become head of the office then a consulting engineer
Founder and editor of the journal Engineering for 60 years
Honorary degree (LL.D) from Glasgow
Bought telescope from George Hunt in 1896
Published 731 mean measures in 5 papers in MNRAS

## Slide 25: Maw’s house Outwood, Surrey

## Slide 27
W. J. Thorrowgood FRAS

## Slide 28: William John Thorrowgood (1862 – 1928)
Signals Engineer on Southern Railway
Bought the telescope in 1927 and installed it in his garden at Wimbledon, London
Died in 1928 and left the telescope and dome to the RAS
On loan to Cambridge in 1929

## Slide 29
Thorrowgood’s dome is till in use 89 years on
Coming to Cambridge

## Slide 31: RETEL micrometer - 1

## Slide 32: RETEL micrometer – 2 Fitted to the 8-inch Cooke refractor at Cambridge.

## Slide 33: Filar micrometer - measurement technique
First setting Second setting

## Slide 34: Cambridge -1
Started 1990 March using a RETEL micrometer
X2.9 Barlow + 18 mm Kellner = x460
12 micron wires subtend 0”.3
Scale = 12”.46 per revolution = 24”.93 per mm
Range of measurement: 0”.4 to 155”
Bright field illumination (red LED)
Magnitude limit: V ~ 10
Dec limit: -20 degrees

## Slide 35: Cambridge - 2
840 nights
9,250 individual measures
2,450 means
1,680 measures of calibration pairs
12 micrometer settings per measure –
4 double distance + 4 angles
(Calibrations: 6 double-distance and 6 angles at beginning
and end of night)

## Slide 36: Cambridge - 3
Calibration pairs from Hipparcos catalogue
RA Dec n scale (“) error(“)
iota Cnc (30”) 0847 +2846 160 24.86 0.14
delta Ori (52”) 0532 -0018 140 24.96 0.12
delta Boo (108”) 1526 +3319 120 25.02 0.10
theta Ser (22”) 1856 +0812 44 24.82 0.13
beta Cyg (34”) 1931 +2758 230 24.94 0.12
alpha CVn (19”) 1256 +3819 116 24.92 0.16
nu Dra (62”) 1732 +5511 50 24.97 0.11
16 Cyg (39”) 1850 +3322 85 24.90 0.12
Weighted mean = 24”.93

## Slide 37
Observing log

## Slide 38: Assessment of measurement accuracy
Compared 1242 mean measures with published astrometry from Hipparcos and speckle
No corrections made for orbital motion –choose similar epochs
Hipparcos and Tycho catalogues (>10”)
USNO speckle : 67-cm
Mason & Hartkopf : 4-metre KP and CT
Tokovinin: 4.2-metre SOAR
Horch: 3.5-metre WIYN
Scardia and Prieur: 1-metre and PISCO camera
Losse – 40-cm

## Slide 39
N = 832

## Slide 40
N = 832

## Slide 41
N = 410

## Slide 42
N = 410

## Slide 43: Samples of binary systems followed
Means taken annually:
STF1110, 1196, 1523, 1536, 1670, 1888, 1909, 1937, 2055,
2084, 2130, 2272, 2758, SHJ345, STF2909, 3050
Every 2 – 3 years
STF73, 202, STT98, STF1037, 1273, 1356, 1865, 1938, 2032,
2052, 2382, 2383, 2579, STT 413, STF2737, 2822, 3062
Every 4 to 5 years
STF 60, 208, 554, 728, STT 545, STF1338, 2262, STT 358,
STF2944

## Slide 44: Xi UMa P = 59.8 years

## Slide 45: 70 Ophiuchi P = 88.3 years

## Slide 46: Zeta Herculis P = 34 years

## Slide 47: Castor P = 466 years

## Slide 48: Gamma Vir P =169.104 years

## Slide 49: Gamma Virginis imaged in 2005 by Damian Peach

## Slide 50: 53 Aqr P = 3500 years (?)

## Slide 51: STF 1196 (zet Cnc AB) P =59.8 years

## Slide 52: Measures of separation in zeta CnC AB-C over 20 years showing perturbation due to Cc

## Slide 53: Measures of position angle of zeta Cnc AB-C showing perturbation of AB by Cc

## Slide 54: Zeta Cancri quadruple system

## Slide 55: Publication of observations
The measures from the 8-inch programme have been published in the Circulars of the Webb Society Double Star Section Nos 5 to 26 and are freely available on:
www.webbsociety.org/double-stars/double-star-section-circulars

## Slide 56: Amateur double star groups
Webb Society Double Star Section Circulars (UK) - annual
Started 1979 – 26 editions – 1650 pages
Journal of Double Star Observations (USA) - quarterly
Founded 2005 - 53 editions - 4250 pages
El Observador de Estrellas Dobles (Spain) - quarterly
Founded 2009 - 21 editions - 1950 pages
Il Bolettino delle Stelle Doppie (Italy) - quarterly
Founded 2012 - 26 editions - 1165 pages
Societe Astronomique de France Double Star Section
Founded 1981 – published in Observations y Travaux

## Slide 57: From the Night Sky – John Larard

## Slide 58: Webb Society Double Star Section
Formed 1968
Double Star Handbook published 1975
Measurement started 1979
Circulars began 1979
Current issue No 26 (2018 – in prep.)
Measures to date: 51,000+

## Slide 60: Cambridge Double Star Atlas 2

## Slide 61: Hartung

## Slide 62: Burnham’s Celestial Handbook (3 vols)

## Slide 63: Haas

## Slide 64: Webb

## Slide 67: USNO 6th orbital catalogue
Grade | Category | Longest period (years) | Pairs | %
1 | Definitive | 88.38 | 52 | 3.6
2 | Good | 257 | 198 | 13.8
3 | Reliable | 522.16 | 292 | 20.4
4 | Preliminary | 18212.2 | 454 | 31.7
5 | Indeterminate | 32000 | 437 | 30.4

## Slide 69: THE END

## Slide 70: Another Thorrowgood telescope